## Slide 1
REPRESENTING CURVES
Bezier Curve

## Slide 2
<number>
CONIC SECTIONS (2D & 2ND DEGREE)
The General Equation for a Conic Section: Ax2 + Bxy + Cy2 + Dx + Ey + F = 0

## Slide 3
<number>
CONIC SECTIONS (2D & 2ND DEGREE)
The type of section can be found from the sign of: B2 - 4AC
If B2 - 4AC is... | then the curve is a...
< 0 | ellipse, circle, point or no curve.
= 0 | parabola, 2 parallel lines, 1 line or no curve.
> 0 | hyperbola or 2 intersecting lines.

## Slide 4: Circle
Cartesian equation: x2 + y2 = a2
Parametrical equation: x = a cos(t), y = a sin(t)

## Slide 5: Ellipse
Cartesian equation: x2/a2 + y2/b2 = 1
Parametrical equation: x = a cos(t), y = b sin(t)

## Slide 6: Parabola
Cartesian equation: y = ax2 + bx + c

## Slide 7: Hyperbola
Cartesian equation: x2/a2 - y2/b2 = 1
Parametrical equation: x = a sec(t) = a/cos(t), y = b tan(t)

## Slide 8
<number>
PARAMETRIC CURVE
explicit form: y = f(x) is computed by the
function f, and the pair of coordinates (x, y)
sweeps out the curve --
A parametric curve: x(t) and y(t). As t varies,
the coordinates (x(t), y(t)) sweep out the curve:
x(t) = sin(t), y(t) = cos(t)
CAGD (Computer Aided Geometric Design)
deals primarily with polynomial or rational
functions, not trigonometric functions:
x(t) = 2t/(1+t*t), y(t)=(1-t*t)/(1+t*t)
Both equations above yield circles, so how do
they differ? It is the parameterization.

## Slide 9
<number>
The slope is given by the tangent line at any
point (x’(t), y’(t)), which determines the speed
the point traces out the curve
t moves the point (x(t), y(t)) along the path of
the curve; the point’s speed varies as t varies
(derivative vector changes in length.)
The motion of the point (x(t), y(t)) is different,
even if the paths (the circles) are the same.

## Slide 10
<number>
PARAMETRIC CUBIC CURVES
In general, a parametric polynomial is written as
Parametric cubics are the lowest-degree curves
that are nonplanar in 3D; generated from an
input set of math functions or data points.
where the curve:
Q(t) = [x(t), y(t), z(t)]
dQ/dt = Q’ is the parametric tangent vector
n
n
t
a
t
a
t
a
a
t
f





2
2
1
0
)
(

## Slide 11
<number>
Continuity condition -- parametric continuity:
Zero-order parametric continuity, C0, means simply that the curves meet. 1st-order parametric continuity, C1, means that the 1st derivatives for two successive curve sections are equal at their joining point:
Second-order parametric continuity, C2, means that both the first and second parametric derivatives of the two curve sections are the same at the intersection:

## Slide 12
<number>
Problems: a particle travels in a straight line,
but has distinct jumps in velocity -- not C
1
, but
the curve is smooth; conversely, a C
1
curve can
have a kink in it when the velocity of the
particle goes to zero where it changes direction
and starts up again.

## Slide 13
<number>
Continuity condition -- geometric continuity:
Zero-order geometric continuity, G0, means simply that the curves meet. 1st-order geometric continuity, G1, means that the 1st derivatives for two successive curve sections are proportional at their joining point. That is, the tangent changes continuously; the directions (but not necessarily the magnitudes) of the two segments’ tangent vectors are equal at a join point:
Second-order geometric continuity, G2, means that both the first and second parametric derivatives of the two curve sections are proportional at the intersection:

## Slide 14
<number>
In general, C
1
implies G
1
, but if a C
1
curve has
a kink because its derivative goes to zero, then
this curve will not be G
1
, since the tangent
direction changes discontinuously at the kink.

## Slide 15: A line segment
blending functions
geometric constraints

## Slide 16
<number>
Hermite Curves
Constraints on the endpoints P1 and P4 and
tangent vectors at endpoints R
1
and R
4
:
We can easily arrive at:

## Slide 17
<number>
Expanding the product gives the Hermite blending functions:
The polynomials Hk(t) for k=0, 1, 2, 3 and referred to as
blending functions because they blend the boundary
constraint values to obtain each coordinate position
along the curve.

## Slide 18: Hermite blending functions
At t=0, only the function H0 is nonzero. As as t becomes
greater than zero, all other blending functions begin to
have an influence.

## Slide 19: Varying the magnitude of the tangent vector
If the directions of the tangent vectors are fixed, the
longer the vectors, the greater their effect on the curve.

## Slide 20: Hermite basis matrix

## Slide 21: Varying the direction of the tangent vector

## Slide 22: Obtaining geometric continuity G1
for parametric continuity C1, k = 1

## Slide 23: Hermite basis matrix

## Slide 24
<number>
Bezier Curve
http://www.cs.princeton.edu/~min/cs426/classes/bezier.html

## Slide 25
<number>
We can easily arrive at:
Bezier Curves
R1=3(P2 - P1), R4=3(P4 - P3) the Bezier curve interpolates the two end control points and approximates the other two. (Multiplay by 3 to have a constant velocity from P1 to P4)
Bezier Curve

## Slide 26
<number>
The curve is cotangent to the control polygon at these
endpoints.
Expanding the product gives the Bernstein polynomials
The sum of the 4 blending polynomials is everywhere unity
and that each polynomial is everywhere nonegative:
Q(t) is just a weighted average of the four control points -- each curve
segment is completely contained in the convex hull of the 4 control points.
The convex-hull property holds for all cubics defined by
weighted sums of control points if the blending functions are
nonnegative & sum to one.

## Slide 27: Bézier curves properties
The convex hull property
Partition of unity
Invariance under affine transformations

## Slide 28
<number>
Bézier Curves of General Degree
Given n+1 control-point positions, we can blend them to
produce the following:
We know:
The binomial coefficient,
is a closed form representation for an entry in
Pascal’s triangle:
Where the Bernstein functions:

## Slide 29: The Bernstein polynomials n=3

## Slide 30: The Bernstein polynomials

## Slide 31
<number>
We can define recursive calculation:
An important characteristic of the Bernstein functions
is the partition of unity:
It is a key to understanding Bézier curves.

## Slide 32
<number>

## Slide 33
<number>
Subdivide of the Curve
The Derivative of the Bézier Curve
One less term in the derivative than in the
original function; the degree of the Bernstein
polynomials is one less.
The control points for the derivative curve are
successive differences of the original curve’s
control points.

## Slide 34
<number>
Natual Cubic Spline Curves
Spline: a flexible strip used to produce a
smooth curve through a designeated set of
points.
A natual cubic spline: cubic curve segments
through the set of points
C2 continuity at the designeated control points
Given n+1 control points, we have n curve
sections and 4n polynomial coefficients
We have 4n-2 equations to be satisfied by the 4n
polynomial coefficients -- we need 2 more
conditions: add a little assumption
Disadvantages moving any one control point affects the
entire curve; the computation time needed

## Slide 35
<number>
Uniform Nonrational B-Splines
Polynomial coefficients depend on just a few control
points. (local control)
Same continuity as natural splines but do not interpolate
their control points.
m+1 control points, P
0
, ..., P
m
, m

3, m-2 cubic
curve segments Q
3
, ..., Q
m
. For m=4:

## Slide 36
<number>
The isotropic constraint is needed to find the
curve equations
Each curve is defined on its own domain 0

t<1.
We can adjust the parameter (t=t+k) so that the
parameter domains for the various curve
segments are sequential: t
i

t<t
i+1
For each i>3, there is a joint point or knot
between Q
i-1
and Q
i
at the parameter value t
i
Uniform -- the knots are spaced at equal
intervals of parameter
t
Nonrational: not ratio of polynomials; rational:
x(t)=X(t)/W(t), y(t)=Y(t)/W(t), z(t)=Z(t)/W(t)
are defined as ratio of two cubic polynomials.
B - “basis.” The spline is weighted sums of basis
functions, in contrast to the natural splines.

## Slide 37
<number>

## Slide 38
<number>
given knots, provided some additional info is
given (tagent vectors at the 2 end knots)
Nonuniform, Nonrational B-Splines
The parameter interval between successive
knot values need not be uniform.
The nonuniform knot-value sequence means
that the blending functions are no longer the
same for each curve interval
Advantages: continuity at selected join points
can be reduced from C
2
to C
1
to C
0
to none; the
resulting curve can be easily reshaped
If the continuity is reduced to C0, then the
curve interpolates a control point without the
undesirable effect of uniform B-splines, where

## Slide 39
<number>
the curve segments on either side of the
interpolated control point are straight lines
Starting & ending points can be interpolated
exactly without introducing linear segments.
Restriction: knot sequence is nondecreasing,
which allows successive knot values equal: a
sequence from t
0
to t
m+4
. The curve is not
defined outside the interval t
3
through t
m+1
.
When ti=ti+1
(a multiple knot), curve segment
Q
i
is a single point, which provides the extra
flexibility of nonuniform B-splines; C
2
to C
1
for
1 extra knot, C
1
to C
0
for 2 extra knots, C
0
to
no continuity for 3 extra knots (multiplicity 4)

## Slide 40
<number>
Nonuniform, Rational Cubic Polynomial Curve Segments
General rational cubic curves are ratios of
polynomials: x(t) = X(t)/W(t), y(t) = Y(t)/W(t),
z(t) = Z(t)/W(t) whose control points are
defined in homogeneous coordinates.
Polynomials can be Bezier, Hermite, or any
other type. When they are B-Splines, called
NURBS
We can also think of the curve as existing in
homogeneous space: Q(t) = [X(t) Y(t) Z(t) W(t)]
Useful for two reasons: 1) invariant under

## Slide 41
<number>
perspective transformation of the control
points (nonrational curves are invariant under
only rotation, scaling, and translations);
The alternative is first to generate
points on the curve itself and then to
apply the perspective transformation to
each point, a far less efficient process
Useful: 2) Unlike nonrationals, they can define
precisely any of the conic sections. This is useful
in CAD, where general curves and surfaces as
well as conics are needed. Both types of entities
can be defined with NURBS.