## Slide 1
RASTER DISPLAYS
Store the primitives in a famebuffer, or refresh
buffer, which is a RAM with 1024*1280, or
V *
H
addressable pixels)
Bitmap -- array of 0/1 (pixels); pixmap -- array
of gray-scale pixels
Monochrome -- bi-level (0/1); gray-scale --
multiple level (0-15); color -- (r, g, b)
Scan-conversion (rasterization) -- objects are
converted into discrete pixels in framebuffer
Aliasing -- jaggies or staircasing of lines/edges;
anti-aliasing
-- dealing with aliasing
Resolution -- # of distinguishable lines per inch.
BASIC GRAPHICS HARDWARE

## Slide 2
CRT (CATHODE RAY TUBE)
LASER PRINTER (HARD COPY DISPLAY DEVICE)
Framebuffer
<number>

## Slide 3
<number>
RASTER DISPLAY SYSTEMS
Graphics card: handle scan-conversion and other advanced graphics functions
Graphics Card (Video Card)

## Slide 4
<number>
Framebuffer (bit planes): RAM with the generated
pixmap and attributes ready for display
Video controller: refresh the display; interlaced
-- fine as long as adjacent scan lines display
similar information;
non-interlaced
(NI)
# of bits for color: direct (RGB mode) and
indirect (Index mode)
Z-buffer (bit planes): corresponding to the framebuffer; depth of each pixel in the framebuffer for hidden surface removal
RGB Mode
Index Mode

## Slide 5
<number>
Double-buffering: don’t display until the entire
scene is rendered
Transformation: calculations of coordinates of
object moving, rotating, and change
Clipping: no imaging system can see the whole
world (internal representation) at once.
Projection: 3D objects are displayed on 2D screen
Output from video controller: RGB, mono- chrome,
or NTSC (National TV System Committee, effective
resolution 350*350); video mixing
RGB, NTSC, SECAM, PAL have different
standards with their own # of scan lines,
frequencies and synchronization.