## Slide 1
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
Texture Lab
TEXTURE MAPPING IN OPENGL
At each rendered pixel, selected texels are used
either to substitute for or to scale one or more
of the surface’s material properties, such as its
diffuse color components.
One pixel is often covered by a number of
texels: nearest pixel, bilinear interpolation,
bi-cubic interpolation, etc.

## Slide 2
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
An Overview
Steps in Texture Mapping
1) Specify the texture. (R, G, B, A, mipmapping)
2) Indicate how the texture is to be applied to each
pixel. (decal, modulate, blend)
3) Enable texture mapping. (glEnable()
GL_TEXTURE_1D or GL_TEXTURE_2D
4) Draw the scene, supplying both texture and
geometric coordinates.
Texture Lab

## Slide 3
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
Texture mapping works only in RGB mode in OpenGL
Example: A Texture-Mapped Checkerboard: checker.c
void makeCheckImage(void)
{ int i, j, c;
for (i = 0; i < checkImageHeight; i++) {
for (j = 0; j < checkImageWidth; j++) {
c = ((((i&0x8)==0)^((j&0x8))==0))*255;
checkImage[i][j][0] = (GLubyte) c;
checkImage[i][j][1] = (GLubyte) c;
checkImage[i][j][2] = (GLubyte) c;
checkImage[i][j][3] = (GLubyte) 255;
}
}
}

## Slide 4
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
void init(void){
makeCheckImage();
glPixelStorei(GL_UNPACK_ALIGNMENT, 1);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_WRAP_S, GL_REPEAT);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_WRAP_T, GL_REPEAT);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MAG_FILTER, GL_NEAREST);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MIN_FILTER, GL_NEAREST);
glTexImage2D(GL_TEXTURE_2D, 0, 4, checkImageWidth, checkImageHeight, 0, GL_RGBA, GL_UNSIGNED_BYTE, checkImage);
}

## Slide 5
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
checker
void display(void)
{
glEnable(GL_TEXTURE_2D);
glTexEnvf(GL_TEXTURE_ENV, GL_TEXTURE_ENV_MODE, GL_DECAL);
glBegin(GL_QUADS);
glTexCoord2f(0.0, 0.0); glVertex3f(-2.0, -1.0, 0.0);
glTexCoord2f(0.0, 1.0); glVertex3f(-2.0, 1.0, 0.0);
glTexCoord2f(1.0, 1.0); glVertex3f(0.0, 1.0, 0.0);
glTexCoord2f(1.0, 0.0); glVertex3f(0.0, -1.0, 0.0);
glTexCoord2f(0.0, 0.0); glVertex3f(1.0, -1.0, 0.0);
glTexCoord2f(0.0, 1.0); glVertex3f(1.0, 1.0, 0.0);
glTexCoord2f(1.0, 1.0); glVertex3f(2.41421, 1.0, -1.41421);
glTexCoord2f(1.0, 0.0); glVertex3f(2.41421, -1.0, -1.41421);
glEnd();
glFlush();
glDisable(GL_TEXTURE_2D);
}

## Slide 6: Texture Interpolation
Specify where the vertices in world space are mapped to in texture space
  s = s (x, y, z)
  t = t (x, y, z)
  Straight lines in world space go to straight lines in texture space
Texture map
s
t
Triangle in world space

## Slide 7: Interpolating texture coordinates for pixels
(x1, y1), (s1, t1)
(x2, y2), (s2, t2)
(x3, y3), (s3, t3)

## Slide 8: Textures
Two-dimensional texture pattern T(s, t)
It is stored in texture memory as an n*m array of texture elements (texels)
  We are interested in mapping the pixel domains (areas) to areas in the texture space

## Slide 9: Transform texture coordinates
All the texture coordinates are multiplied by Gl_TEXTURE matrix before in use
To transform texture coordinates, you do:
  glMatrixMode(Gl_TEXTURE);

## Slide 10: Texture Mapping
Texture mapping is done as the primitives are rasterized

## Slide 11: 4.6.texture.c
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
void initTexture(void)
{
read_stars_image();
glPixelStorei(GL_UNPACK_ALIGNMENT, 1);
// glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_WRAP_S, GL_REPEAT);
// glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_WRAP_T, GL_REPEAT);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MAG_FILTER, GL_NEAREST);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MIN_FILTER, GL_NEAREST);
glTexImage2D(GL_TEXTURE_2D, 0, GL_LUMINANCE, stars_pixels, stars_pixels,
0, GL_LUMINANCE, GL_UNSIGNED_BYTE, stars_image);
}
Texture

## Slide 12: 4.6.texture.c
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
void drawTexture(float x, float y, float z)
{
// glRasterPos3f(x, y, z);
glTexEnvf(GL_TEXTURE_ENV, GL_TEXTURE_ENV_MODE, GL_REPLACE);
glEnable(GL_TEXTURE_2D);
glBegin(GL_QUADS);
glTexCoord2f(0.0, 0.0); glVertex3f(x, y, z);
glTexCoord2f(0.0, 1.0); glVertex3f(-x, y, z);
glTexCoord2f(1.0, 1.0); glVertex3f(-x, -y, z);
glTexCoord2f(1.0, 0.0); glVertex3f(x, -y, z);
glEnd();
glDisable(GL_TEXTURE_2D);
}
Texture

## Slide 13: 4.6.texture.c
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
void display(void)
{
drawTexture(-2.4*Width, -2.4*Height, -1.9*Width);
drawRobot(A, B, C, alpha, beta, gama);
glutSwapBuffers();
}
Texture

## Slide 14
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
Specifying the Texture
void glTexImage2D(GLenum target, GLint level,
GLint components, GLsizei width, GLsizei height,
GLint border, GLenum format, GLenum type, const GLvoid *pixels);
1) The target parameter: constant GL_TEXTURE_2D.
2) The level parameter for multiple resolutions
3) Components is 1 of 38 symbolic constants. A value of 1
selects the R component, 2 selects the R and A
components, 3 selects R, G, and B, and 4 selects R,
B, G, and A. It indicates which values are selected for texels
4) The width and height parameters give the
dimensions of the texture image.
5) The border indicates the width of the border, which
is usually zero.
6) The format and type parameters describe the format
and data type of the texture image data.
(GL_COLOR_INDEX, GL_RGB, GL_RGBA, GL_RED,
GL_GREEN, GL_BLUE, GL_ALPHA,
GL_LUMINANCE, or GL_LUMINANCE_ALPHA,
corresponding to 3)

## Slide 15
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
The number of texels for both the width and height of a texture image, not including the optional border, must be a power of 2.
gluScaleImage() correct/alter the sizes of your textures
glCopyTexImage2D() creates a 2D texture using framebuffer data
1D textures and 3D textures
3D textures are used for rendering in medical and geoscience applications (CT or MRI images)
  void glTexImage1D()
  void glTexImage3D()
Some Minor Things

## Slide 16: Pixel and Texel Relations
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
Corresponding vertices of texture and polygons
glBegin(GL_QUADS);
glTexCoord2f(0.0, 0.0); glVertex3f(x, y, z);
glTexCoord2f(0.0, 1.0); glVertex3f(-x, y, z);
glTexCoord2f(1.0, 1.0); glVertex3f(-x, -y, z);
glTexCoord2f(1.0, 0.0); glVertex3f(x, -y, z);
Antialiasing
  Pre-filtering: Filter the texture down before applying it
  Post-filtering: Take multiple pixels from the texture and filter them before applying to the polygon fragment
Texel color components replace or modulate pixel color
  GL_MODULATE – multiply texture and object color
  GL_BLEND – linear combination of texture and object color
  GL_REPLACE – use texture color to replace object color

## Slide 17: Antialiasing
Pre-filtering: Filter the texture down before applying it
Post-filtering: Take multiple pixels from the texture and filter them before applying to the polygon fragment

## Slide 18: Multiple Levels of Detail (Pre-filtering)
textures that are mapped onto smaller objects might shimmer and flash as the objects move.
To use mipmapping, you provide all sizes of your texture in powers of 2 between the largest size and a 1x1 map.
OpenGL chooses matching size for texture mapping
Mipmapping requires some extra computation and texture storage area;

## Slide 19
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
A Mipmapping Example: mipmap.c
A Mipmapping Example: mipmap.c
void myinit(void) {
... ;
loadImages();
glPixelStorei(GL_UNPACK_ALIGNMENT, 1);
glTexImage2D(GL_TEXTURE_2D, 0, 3, 32, 32, 0,
GL_RGB, GL_UNSIGNED_BYTE, &mipmapImage32[0][0][0]);
glTexImage2D(GL_TEXTURE_2D, 1, 3, 16, 16, 0,
GL_RGB, GL_UNSIGNED_BYTE, &mipmapImage16[0][0][0]);
...
glTexParameterf(GL_TEXTURE_2D,
GL_TEXTURE_MAG_FILTER, GL_NEAREST);
glTexParameterf(GL_TEXTURE_2D,
GL_TEXTURE_MIN_FILTER, GL_NEAREST_MIPMAP_NEAREST);
mipmap
}

## Slide 20: Mipmap Math
Define a scale factor,  = texels/pixel
  It can be derived from the transformation matrices
Define =log2 
 tells you which mipmap level to use
  Level 0 is the original texture, level 1 is the next smallest texture, and so on
  If <0, then multiple pixels map to one texel: magnification

## Slide 21: Post-Filtering
Magnification: When <0 the image pixel is smaller than the texel:
  glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MAG_FILTER, type)
  Type is GL_LINEAR or GL_NEAREST
Minification: When >0 the image pixel is bigger than the texel:
  GL_TEX_MIN_FILTER
  Can choose to:
    Take nearest point in base texture, GL_NEAREST
    Linearly interpolate nearest 4 texels in base texture, GL_LINEAR
    Take the nearest mipmap and then take nearest or interpolate in that mipmap, GL_LINEAR_MIPMAP_NEAREST
    Interpolate between the two nearest mipmaps using nearest or interpolated points from each, GL_LINEAR_MIPMAP_LINEAR

## Slide 22
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
Controlling Filtering

## Slide 23
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
glTexParameteri(GL_TEXTURE_2D
GL_TEXTURE_MAG_FILTER, GL_NEAREST);
glTexParameteri(GL_TEXTURE_2D
GL_TEXTURE_MIN_FILTER, GL_NEAREST);
Parameter
Values
GL_TEXTURE_MAG_FILTER
GL_NEAREST or
GL_LINEAR
GL_TEXTURE_MIN_FILTER
GL_NEAREST,
GL_LINEAR,
GL_NEAREST_MIPMP_NEAREST,
GL_NEAREST_MIPMP_LINEAR,
GL_LINEAR_MIPMAP_NEAREST, or
GL_LINEAR_MIPMAP_LINEAR

## Slide 24: Trilinear filtering
Trilinear filtering is an extension of the bilinear texture filtering method, which also performs linear interpolation between mipmaps.

## Slide 25: Anisotropic filtering
With RIP mapping (rectim in parvo) for a 256x256 image, images are also sampled to 256x128 and 32x128 etc.
  These anisotropically downloadsampled images are used when the texture mapped image frequency is different for each texture axis
  RIP mapping has a limitation in that it only supports anisotropic probes that are axis aligned in texture space.
  This results in blurriness when the textured surface is at an oblique angle - a very common case is the floor as it recedes into the distance. Anisotropic filtering corrects this by sampling in the correct trapezoid shape according to view angle. The resulting samples are then trilinearly filtered to generate the final color.

## Slide 26
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
Texturing Functions
void glTexEnv{if}{v}(GLenum target, GLenum pname, TYPE param);
target must be GL_TEXTURE_ENV.
If pname is GL_TEXTURE_ENV_MODE, param can be GL_DECAL, GL_REPLACE, GL_MODULATE, or GL_BLEND, to specify how texture values are combined with the color values of the fragment.
If pname is GL_TEXTURE_ENV_COLOR, param is an array of four floating-point values representing R, G, B, and A components, used only if the GL_BLEND texture function has been specified as well.
Components Decal Mode Modulate Mode Blend Mode
1 undefined C = LtCf, C = (1-Lt)Cf + LtCc,
A = Af A = Af
2 undefined C = LtCf, C = (1-Lt)Cf + LtCc,
A = At Af A = At Af
3 C = Ct C = CtCf , undefined
A = Af A = Af
4 C = (1-At)Cf + AtCt, C = CtCf , undefined
A = Af A = AtAf
Note: t -- texture, f -- fragment, c -- the values assigned with GL_TEXTURE_ENV_COLOR
Texture Lab

## Slide 27
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
Texture Objects
Generate texture objects or names: glGenTextures()
Initially bind texture objects to texture data, including the image arrays and texture properties: glBindTexture()
More often used objects stay in memory (prioritize the objects).
Bind and rebind texture objects, making their data available for rendering texture models
When we call glBindTexture() with a texture name, all subsequent glTex*() commands that specify the texture and its associated parameters are saved in the memory

## Slide 28: 4.7.texobjects.c
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
Texture

## Slide 29
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
Assigning Texture Coordinates
Texture coordinates can comprise one, two, three, or
four coordinates. They’re usually referred to as the
s, t, r, and q coordinates.
For one-dimensional textures, you use the s
coordinate; for two-dimensional textures, you use s
and t.
The q, like w, is typically given the value 1 and can be used
to create homogeneous coordinates
The command to specify texture coordinates,
glTexCoord*(), is similar to glVertex*(), glColor*(),
and glNormal*(). Usually, texture-coordinate values
range between 0 and 1; values can be assigned
outside this range, however, with the results
described in “Repeating and Clamping Textures.”
void glTexCoord{1234}{sifd}{v}(TYPEcoords);
Texture Lab

## Slide 30: Computing Approximate Texture Coordinates
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
Polygon aspect ratio 3/2 (w/h); texture aspect ration 1. To avoid distorting the texture: use texture coordinates of (0,0), (1,0), (1,2/3), (0,2/3)
A can with label 4 units tall and 12 units around (aspect ratio 3/1). Textures must have aspect ratio of 2n to 1. We can copy and paste it twice to make an aspect ration of 1. Let’s approximate the can by 30 (4*12/30) polygons. We can use the following texture coordinates:
  (0,0), (1/30,0), (1/30,1/3),(0,1/3)
  (1/30,0), (2/30,0), (2/30,1/3),(1/30,1/3)
  …
  (29/30,0), (1,0), (1,1/3),(29/30,1/3)
Only a few curved surfaces (cone and cylinders) can be mapped to a flat surface without geodesic distortion. For example, a sphere (coscos,cossin,sin). The - rectangle can be mapped directly to a rectangular texture map, but the closer you get to the poles, the more distorted the texture.

## Slide 31
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
Repeating and Clamping Textures
You can assign texture coordinates outside the
range [0,1] and have them either clamp or repeat.
With repeating textures, if you have a large plane
with texture coordinates running from 0.0 to 10.0 in
both directions, for example, you’ll get 100 copies of
the texture tiled together on the screen.
For most applications where the texture is to be
repeated, the texels at the top of the texture should
match those at the bottom, and similarly for the left
and right edges.
To clamp the texture coordinates: Any values
greater than 1.0 are set to 1.0, and any values less
than 0.0 are set to 0.0. Clamping is useful for
applications where you want a single copy of the
texture to appear on a large surface.
If the surface-texture coordinates range from 0.0 to
10.0 in both directions, one copy of the texture
appears in the lower corner of the surface. The rest
of the surface is painted with the texture’s border
colors as needed.
Texture Lab

## Slide 32
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
glBegin(GL_POLYGON);
glTexCoord2f(0.0, 0.0); glVertex3f(-2.0, -1.0, 0.0)
glTexCoord2f(0.0, 3.0); glVertex3f(-2.0, 1.0, 0.0);
glTexCoord2f(3.0, 3.0); glVertex3f(0.0, 1.0, 0.0);
glTexCoord2f(3.0, 0.0); glVertex3f(0.0, -1.0, 0.0);
glEnd();
glBegin(GL_POLYGON);
glTexCoord2f(0.0, 0.0); glVertex3f(1.0, -1.0, 0.0);
glTexCoord2f(0.0, 3.0); glVertex3f(1.0, 1.0, 0.0);
glTexCoord2f(3.0, 3.0); glVertex3f(2.41421, 1.0, -1.41421);
glTexCoord2f(3.0, 0.0); glVertex3f(2.41421, -1.0, -1.41421);
glEnd();

## Slide 33
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
<number>
glTexParameterfv(GL_TEXTURE_2D, GL_TEXTURE_S_WRAP GL_REPEAT);
glTexParameterfv(GL_TEXTURE_2D, GL_TEXTURE_T_WRAP GL_REPEAT);
or
glTexParameterfv(GL_TEXTURE_2D, GL_TEXTURE_S_WRAP GL_CLAMP);
glTexParameterfv(GL_TEXTURE_2D, GL_TEXTURE_T_WRAP GL_CLAMP);
You can also clamp in one direction and repeat in the other.

## Slide 34: OpenGL texture mapping
1) Specify texture
    read or generate image; gluScaleImage();
    Assign to texture
    glTeximage2D(GL_TEXTURE_2D, 0, GL_RGB, 64, 64, 0, GL_RGB, GL_UNSIGNED_BYTE, myImage);
  2) Specify texture mapping parameters
    Wrapping, filtering, how to combine pixel and texel, etc.
  3) Enable GL texture mapping (GL_TEXTURE_2D)
  4) Assign texture coordinates to vertices
  5) Transform texture coordinates
  5) Draw your objects
  6) Disable GL texture mapping

## Slide 35: Put it all together
…
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_WRAP_S, GL_REPEAT);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_WRAP_T, GL_REPEAT);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MAG_FILTER, GL_NEAREST);
glTexParameteri(GL_TEXTURE_2D, GL_TEXTURE_MIN_FILTER, GL_NEAREST);
glTexEnvf(GL_TEXTURE_ENV, GL_TEXTURE_ENV_MODE, GL_REPLACE);
…
glEnable(GL_TEXTURE_2D);
glTexImage2D(GL_TEXTURE_2D, 0, GL_RGB, 64, 64, 0, GL_RGB, GL_UNSIGNED_BYTE, mytexture);
Draw_picture1(); // define texture coordinates and vertices in the function
….

## Slide 36: Automatic Texture-Coordinate Generation
Copyright @ 2002 by Jim X. Chen: jchen@cs.gmu.edu
To make contours on a 3D model
to simulate reflections from an arbitrary environment on a shiny model
  glTexGen*(Glenum coord, Glenum pname, TYPE param);
  glTexGen*v(Glenum coord, Glenum pname, TYPE *param);
Teapot
Control Keys
E, O, S, X
GL_S or GL_T; coord to be auto. generated
GL_TEXTURE_GEN_MODE
GL_OBJECT_PLANE GL_EYE_PLANE
GL_OBJECT_LINEAR, GL_EYE_LINEAR, or GL_SPHERE_MAP
If eye_plane, modelview matrix may not be the same when the polygon vertices are transformed. This function establishes a field of texture coordinates that can produce dynamic contour lines on moving objects.

## Slide 37: Automatic Texture-Coordinate Generation
1st: specify the texture coordinate generation functions for S and T:
  glTexGeni( GL_S, GL_TEXTURE_GEN_MODE, GL_OBJECT_LINEAR );
  glTexGeni( GL_T, GL_TEXTURE_GEN_MODE, GL_OBJECT_LINEAR );
2nd: enable texture coordinate generation:
  glEnable( GL_TEXTURE_GEN_S );
  glEnable( GL_TEXTURE_GEN_T );
3rd: generate the texture coordinates. For object or eye linear, they are based on a reference plane:
  static GLfloat sgenparams[] = { 2, 0, 0, 0 };
  static GLfloat tgenparams[] = { 0, 1, 0, 0 };
  glTexGenfv( GL_S, GL_OBJECT_PLANE, sgenparams );
  glTexGenfv( GL_T, GL_OBJECT_PLANE, tgenparams );

## Slide 38: Perspective correction
Equal spacing in screen (pixel) space is not the same as in texture space in perspective projection
  Perspective foreshortening
from Hill
courtesy of
H. Pfister

## Slide 39: Perspective-Correct Texture Coordinate Interpolation
Interpolate (tex_coord/w) over the polygon, then do perspective divide after interpolation
Compute at each vertex after perspective transformation
  “Numerators” s/w, t/w
  “Denominator” 1/w
Linearly interpolate 1/w, s/w, and t/w across the polygon
At each pixel
  Perform perspective division of interpolated texture coordinates (s/w, t/w) by interpolated 1/w (i.e., numerator over denominator) to get (s, t)

## Slide 40: Perspective Correction Hint
Texture coordinate and color interpolation:
  Linearly in screen space (wrong) OR
  Persective correct interpolation (slower)
glHint (GL_PERSPECTIVE_CORRECTION_HINT, hint), where hint is one of:
    GL_NICEST: Perspective
    GL_FASTEST: Linear
    GL_DONT_CARE: Linear